The Discrete Fourier Transform
The Discrete Fourier Transform
and
the Short-time Fourier Transform
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
[Speaker Notes: Welcome again to the course on Audio Signal Processing for Music Applications!! In this lecture I start with our most fundamental topic, the Discrete Fourier Transform. If you can follow and understand this topic you should have no problem in following the whole course. I divided this topic in two lectures, this is the first one.]

---
Discrete Fourier Transform
Discrete Fourier Transform
{alignl {X[k] = sum from{n=0} to{N-1} {x[n] e^{-j 2%pi kn/N}}~~k=0,..., N-1}} newline newline {alignl {n: "discrete time index" ("normalized time," ~ T=1)}}newline {alignl {k: "discrete frequency index"}}newline {alignl {%omega_k = 2 %pi k / N: "frequency in radians"}}newline {alignl {f_k = f_s k / N: "frequency in Hz" (f_s:"sampling rate")}}
[Speaker Notes: This is it!!! This is the most important equation to be shown in the whole course. So, pay attention!! ... This equation can be decomposed into two parts: the complex exponential and the dot product.]

---
[Speaker Notes: Here we show an input signal, x[n], and the output of the DFT, X[k], the spectrum. it is a real sound, a fragment of an oboe sound. ...]

---
DFT: complex exponentials
alignl {s^{"*"}_{k}= e^{-j2{%pi}kn/N} = cos(2 %pi kn/N) - j sin(2 %pi kn/N)}newline newline alignl {"for" N=4, ~ "thus for" ~n=0,1,2,3; ~k=0,1,2,3} newline newline alignl {s^{"*"}_{0} = cos(2 %pi times 0 times n/4) - j sin(2 %pi times 0 times n/4)=[1,1,1,1]} newline alignl {s^{"*"}_{1} = cos(2 %pi times 1 times n/4) - j sin(2 %pi times 1 times n/4)=[1,-j,-1,j]}newline alignl {s^{"*"}_{2} = cos(2 %pi times 2 times n/4) - j sin(2 %pi times 2 times n/4)=[1,-1,1,-1]} newline alignl {s^{"*"}_{3} = cos(2 %pi times 3 times n/4) - j sin(2 %pi times 3 times n/4)=[1,j,-1,-j]}
[Speaker Notes: As we said, in the DFT equation the input signal x[n] is multiplied by a series of complex exponentials, complex sinewaves. These sinewaves are the basis functions of the DFT, the components that we will identify and measure in the input signal. ... A signal of size N=4 will be projected into 4 sinewaves of size 4.]

---
DFT: complex exponentials
[Speaker Notes: If the signal has a size N=8 we will need 8 complex sinewaves, like these ones. ...]

---
DFT: scalar product
langle {x, s_k} rangle = sum from{n=0} to {N-1} x[n]s^{"*"}_k[n] = sum from{n=0} to {N-1} x[n] e^{-j2{%pi}kn/N}
Example:
alignl {x[n]=[1,-1,1,-1]; N=4} newline newline alignl {langle {x, s_0} rangle = 1 times 1 + (-1) times 1+ 1 times 1+ (-1) times 1 = 0} newline alignl {langle {x, s_1} rangle = 1 times 1 + (-1) times (-j)+ 1 times (-1)+ (-1) times j = 0} newline alignl {langle {x, s_2} rangle = 1 times 1 + (-1) times (-1)+ 1 times 1+ (-1) times (-1) = 4} newline alignl {langle {x, s_3} rangle = 1 times 1 + (-1) times j + 1 times (-1)+ (-1) times (-j) = 0}
[Speaker Notes: The DFT equation can also be expressed by this equation, which emphasizes the scalar product operation of the input signal x[n] by the N complex sinewaves. ...]

---
DFT: scalar product
[Speaker Notes: This is an example of the scalar product operation, of the DFT of a simple sequence. ... This is the DFT operation.]

---
DFT of real sinusoids
alignl {x_3[n]= A_0 cos (2%pi k_0 n/N) = {A_0} over {2} e^{j2%pi k_0 n /N}+ {A_0} over {2} e^{-j2%pi k_0 n/N}}
alignl{X_3[k] = sum from{n=-N/2} to{N/2-1} {x_3[n] e^{-j 2%pi kn/N}}} newline alignl{~~~~~= sum from{n=-N/2} to{N/2-1}({A_0} over {2} e^{j2%pi k_0 n / N}+ {A_0} over {2} e^{-j2%pi k_0 n/N}) {e^{-j 2%pi kn/N}}}newline alignl{~~~~~= sum from{n=-N/2} to{N/2-1}{{A_0} over {2}} e^{j2%pi k_0 n / N} {e^{-j 2%pi kn/N}} + sum from{n=-N/2} to{N/2-1} {{A_0} over {2}} e^{-j2%pi k_0 n/N} {e^{-j 2%pi kn/N}}}newline alignl{~~~~~= sum from{n=-N/2} to{N/2-1}{{A_0} over {2}} e^{-j2%pi (k-k_0) n / N} + sum from{n=-N/2} to{N/2-1} {{A_0} over {2}} e^{-j2%pi (k+k_0) n/N}}newline alignl{~~~~~= {N{A_0} over {2}} "for" k=k_0, -k_0; 0 "for rest of" k}
[Speaker Notes: Let's go a step further and compute the DFT of a real sinusoid, not of a complex one, thus closer to the reality of sounds. A bit more messy!! ... and let's see a plot of it.]

---
[Speaker Notes: This shows what is the output of calculating the DFT of a real sinewave. ... Still we do not find sinusoids like this in our daily life, but we are gettig quite close. Some sounds are not that different to this.]

---
Inverse DFT
x[n] = {1} over {N} sum from{k=0} to {N-1} X[k] s_k[n] = {1} over {N} sum from{k=0} to {N-1} X[k] e^{j2{%pi}kn/N}~n=0,1,...,N-1
Example:
alignl {X[k]=[0,4,0,0]; N=4} newline newline alignl {x[0]= 1 over 4 (X * s) [n=0] = 1 over 4 (0*1 + 4*1+ 0*1+ 0*1) =1} newline alignl {x[1]= 1 over 4 (X * s) [n=1] = 1 over 4 (0*1 + 4*j+ 0*(-1)+ 0*(-j)) = j} newline alignl {x[2]= 1 over 4 (X * s)[n=2] = 1 over 4 (0*1 + 4*(-1)+ 0*1+ 0*(-1)) = -1} newline alignl {x[3]= 1 over 4 (X * s)[n=3] = 1 over 4(0*1 + 4*(-j)+ 0*(-1)+ 0*j) = -j}
[Speaker Notes: One of the great properties of the DFT is that is invertible, which means that we can get back the original signal from its spectrum. ...]

---
Inverse DFT for real signals
alignl {X[k] = abs{X[k]}e^{j<X[k]} ~"and"~ X[-k] = abs{X[k]}e^{-j<X[k]}}newline alignl {"for" ~k=0,1,...,N/2} newline
[Speaker Notes: For real signals we do not need to have the complete spectrum in order to recover the original signal. It is enough to have half of the spectrum, tipically we use the positive side. ... We will come back to these concept in the next lectures.]

---
Introduction: STFT
Short-time Fourier Transform
X_l[k] = sum from{n=-N/2} to{N/2-1} w[n]{x[n+lH] e^{-j 2%pi kn/N}}~~l=0,1,...,
w: analysis window
l: frame number
H: hop-size
[Speaker Notes: This is the Short-time Fourier transform equation, basically a modified version of the DFT, with few but important differences. ... To emphasize the idea of zero-phase windowing we specify the time index n to go from -N/2 to N/2-1.]

---
xw_l[n] = w[n]x[n+lH] ~~~~l=0,1,...,
[Speaker Notes: The windowing process is a way to step through a sound. If we use the analogy of image and video we could relate a spectrum with a photograph, a static image, and the STFT with a video, a time varying image. ...]

---
Transform of a windowed sinewave
alignl {x[n]= A_0 cos (2%pi k_0 n/N) = {A_0} over {2} e^{j2%pi k_0 n /N}+ {A_0} over {2} e^{-j2%pi k_0 n/N}}
alignl{X[k] = sum from{n=-N/2} to{N/2-1} {w[n] x[n] e^{-j 2%pi kn/N}}} newline alignl{~~~~~= sum from{n=-N/2} to{N/2-1}w[n] ({A_0} over {2} e^{j2%pi k_0 n / N}+ {A_0} over {2} e^{-j2%pi k_0 n/N}) {e^{-j 2%pi kn/N}}}newline alignl{~~~~~= sum from{n=-N/2} to{N/2-1}{w[n]{A_0} over {2}} e^{j2%pi k_0 n / N} {e^{-j 2%pi kn/N}} + sum from{n=-N/2} to{N/2-1} {w[n]{A_0} over {2}} e^{-j2%pi k_0 n/N} {e^{-j 2%pi kn/N}}}newline alignl{~~~~~= {{A_0} over {2}} sum from{n=-N/2} to{N/2-1}w[n] e^{-j2%pi (k-k_0) n / N} + {{A_0} over {2}} sum from{n=-N/2} to{N/2-1} w[n] e^{-j2%pi (k+k_0) n/N}}newline alignl{~~~~~= {{A_0} over {2}} W[k-k_0] + {{A_0} over {2}} W[k+k_0]}
[Speaker Notes: To better understand the effect of windowing a sound, lets put an example of what happends when we window a real sinusoid and then compute its spectrum. ...]

---
[Speaker Notes: With these plots we can understand the windowing process better. ... From this discussion we can realize the importance of the analysis window in the spectrum of a sinusoid and thus of any sound. It is clear that we have to spend some time explaining the windows.]

---
Rectangular window
alignl{W[k]= {alignc {sin(%pi k) }} over {alignc {sin(%pi k / M)} }} newline
alignl{ w[n]= 1, ~~n = -M/2, ...,0,...M/2 } newline alignl{ ~ ~ ~~~=0, ~~n = "elsewhere"}
main-lobe width: 2 bins
side-lobe level: -13.3 dB
[Speaker Notes: We start by showing, again, the rectangular window. ...]

---
Hanning window
alignl{ w[n]=.5 + .5 cos(2 %pi n / M), ~n = -M/2, ...,0,...M/2 }
alignl{W[k]=.5 D[k]+ .25(D[k-1]+D[k+1]) ~ "where" D[k]= {alignc {sin(%pi k) }} over {alignc {sin(%pi k / M)}}}
main-lobe width: 4 bins
side-lobe level: -31.5 dB
[Speaker Notes: Maybe the most popular window is the hanning window, which is a raised cosine. ...]

---
[Speaker Notes: This is an example of applying different windows to the same sound fragment. ...]

---
Time-frequency compromise
[Speaker Notes: Now we can put all these concepts together to analyze a real and complex signal, like a piano phrase. Choosing all parameters in the STFT has a number of effects in the output, the most important one is what we call the time-frequency compromise. ...]

---
Amplitude and phase spectrogram
[Speaker Notes: Typically we only show the amplitude, or magnitude, spectrogram, but the phase has also valuable information about the sound. ....]

---
Inverse STFT
Inverse STFT
alignl{y[n] = sum from{l=0} to{L-1} Shift_{lH,n} {[{1 over N}{sum from{k=-N/2} to{N/2-1} X_l[k] e^{j 2%pi kn/N}}]}}
each output frame is:
alignl{yw_l[n] = x(n+lH)w[n]}
and the output sound is:
alignl{y[n] = sum from {l=0} to {L-1} yw_l[n] = x[n]sum from {l=0} to {L-1} w[n-lH]}
[Speaker Notes: Like the DFT, the STFT has the inverse transform. If we do the things right we can recover the original sound from the amplitude and phase spectrogram. ...]

---
[Speaker Notes: Let's show and example. From a complete sound, which varies in time, we can get a spectrogram, and then recover it. ...]

---
References and credits
- More information in:https://en.wikipedia.org/wiki/Discrete_Fourier_transform
  https://en.wikipedia.org/wiki/STFThttps://en.wikipedia.org/wiki/Window_function
- References by Julius O. Smith:https://ccrma.stanford.edu/~jos/mdft/https://ccrma.stanford.edu/~jos/sasp/
- Slides and code released using the CC Attribution-Noncommercial-Share Alike license or the Affero GPL license.
[Speaker Notes: There is a lot of signal processing literature on windows. ...]